## Slide 1: Maths

## Slide 2: CheckSum
Suppose the following block of 16 bits is to be sent using a checksum of bits. The sending 16 bits is 10101001 00111001 . And receiver receive pattern is 10101001 00111001 00011100.
Find if there has any error or not.
  Ans:
  The numbers are added
  10101001
  00111001 -------------
  Sum 11100010
  Checksum 00011101 ; complemented
  The pattern sent is 10101001 00111001 00011101

## Slide 3: Continue
Now the receiver received pattern is
10101001 00111001 00011100
When the receiver adds the three sections, if it will get all 1s,
which, after complementing, is all 0s and then it means that there
is no error otherwise it indicates an error.
10101001
00111001
00011100
Sum : 11111110
Complement 00000001
Means that there is error or packet loss during transmission.

## Slide 4
What Will be transmitted frame if generator is X3+X2+1 and frame is 101100111.
