## Slide 1: DHCP,RIP and Others

## Slide 2: What is DHCP ?
DHCP: Dynamic Host Configuration Protocol
Dynamic Host Configuration Protocol
  Used for dynamic allocation of IP addresses
    used for hosts that run only client applications
  Allows for host-specific configuration parameters to be delivered from a DHCP server to a host
DHCP can also be used to convey permanent IP address assignments to hosts
  Server interfaces need permanent addresses because clients need to be able to reach them
  Also, router interfaces should have permanent addresses for stability of routing data

## Slide 3: Steps of DHCP
DHCP DISCOVER : Newly connected node send a message to all connected nodes and asking for a IP address.
DHCP OFFER : Server offer an IP address to new host by broadcasting the message.
DHCP Request : Now the new node send DHCP request to all nodes that which IP it wants to use. Its also a broadcast message.
DHCP ACKNOWLEDGEMENT : At last DHCP server confirm the host that it can start using the IP address.

## Slide 4: What is RIP
RIP means Routing Information Protocol.
RIP is a routing protocol for exchanging routing table information between routers.
  Routing updates must be passed between routers so that they can make the proper choice on how to route a packet.
What is RIP. Explain with proper example?

## Slide 5
Q. What is Server?
That response to the request.
Q. What Is Gateway?
Gateway is a device that connect two devices of two difference
connection oriented protocol.
Ex. Communication between TCP with ATM protocol.
Q. What is Firewall?
Firewall prevent unauthorized user onto the network.

## Slide 6
Supernetting vs Subnetting?
Subnetting is the process of dividing an IP network in to sub divisions called subnets whereas, Supernetting is the process of combining several IP networks with a common network prefix.
Supernetting will reduce the number of entries in a routing table and also will simplify the routing process.
In subnetting, host ID bits (for IP addresses from a single network ID) are borrowed to be used as a subnet ID, while in supernetting, bits from the network ID are borrowed to be used as the host ID.

## Slide 7
Definition: SMTP, FTP, HTTP, WWW.
Proxy server : In computer networks, a proxy server is a server (a computer system or an application) that acts as an intermediary for requests from clients seeking resources from other servers.

## Slide 8
Troubleshoot : Network troubleshooting is the collective measures and processes used to identify, diagnose and resolve problems and issues within a computer network. It is a systematic process that aims to resolve problems and restore normal network operations within the network.
DB server : is the term used to refer to the back-end system of a database application using client/server architecture. The back-end, sometimes called a database server, performs tasks such as data analysis, storage, data manipulation, archiving, and other non-user specific tasks.
Network Monitoring : Network monitoring is the use of a system that constantly monitors a computer network for slow or failing components and that notifies the network administrator (via email, SMS or other alarms) in case of outages. Network monitoring is part of network management.

## Slide 9
Needs can always be met but greed can never be fulfilled.
….Rajnikanth